## Slide 1: Title
Students’ name
Notes: Hello everyone
when people are designing a so call accelerator, what they usually think about is that how to achieve higher performance, while using less area and power, and these are also my design motivation. Today’s presentation, I’ll try to show you how I achieve this targets in this proposed asynchronous SNN accelerator with a mesh network on chip.

## Slide 2
Outline for Reference
NoC Architecture
Processing Element
Routing
Gate-level Implementation
Verification & Analysis
Advance Design Sparse-Input-Optimized PE
Summary & Outlook
Notes: Before we start, let me give a brief introduction about the topics and contents. In the following part, I’ll talk about the overall architecture and control, followed by the microarchitecture of each functional module. verification and performance analysis of the design, and some improvement made based on the original design.
So lets start from the NoC architecture.

## Slide 3
NoC Architecture
Notes: As mentioned before, the whole accelerator is implemented as network on chip structure with the mesh topology. There are 9 processing element and one memory, all adjacent nodes are connected by links. Unlike common design, there is no separate adders which are responsible for adding the partial sums and generated output spikes. These tasks will be done by each processing element.
So, let’s look in some details about the operation flow. The very first step will be data distribution from the memory. Memory reading suffers from high latency, so data-reuse will be important. The memory send data to some certain nodes, data sharing will then be performed within the whole system to ensure all modules can get required data. Let’s look at the first three pes, they just help each other by calculating the partial sum. Basically, each of the three PEs is required to do same tasks, calculating two partial sums, and generate one output spikes. Only difference is the sequence of doing each tasks. The animation further demonstrate this process.

## Slide 4
Processing Element
Notes: The processing element is like the neuron in the whole neural network. Some blocks and control logic are added to enable compute both partial sum and spike. The merge will decide whether let the partial sums or the results of the multiplier into the adder, according to different operating stage.
Although the PE will do more job, only few changes should be made in our PE. Don’t even need to implement another adder. While for the whole system, the elimination of several node definitely reduce the chip area. And thanks to the asynchronous design, event-driven control flow can be achieved within the NoC system. Each PE does not need to be controlled by a central control unit, but itself controlled, just waiting for input data and then it know what it should do for next step.

## Slide 5
Routing
Notes: As for the router, nothing more than several switches and arbitrated merge implemented in each port. There are five input and output ports, connecting to different nodes and also the PE. The routing algorithm using ere is a simple north last routing, which prohibit the transmission from south port to west or east port. From the turn model, the cycle is broken, which make sure the routing is deadlock-free. It is deterministic routing algorithm, it means all the path are determined, packets are not able to choose other way when traffic jam is happened. But the implementation will be simple, and since in this network on chip, data transmission between nodes will not be too often to cause the traffic congestion. This will be proved from the traffic analysis in later part.

## Slide 6
Gate-level Implementation
Notes: Moreover, this slide shows the

## Slide 7
Verification &
Analysis
Golden Outputs:
Transcript:
Dump file:
 | Results
Cumulative time (Regular) (ns) | 
Operating time (per step) (ns) | 
PE Operating time (ns) | max: min :
Performance:
Notes: Verifications were done to make sure the whole design works fine . Part of the dump file….. ….each function is operated normal. The performance of the accelerator is characterized, list in this table. The PE operating time is the time used for computing, which to a certain extent reflects the PE utilization. From the results, it can be seen that some of the processing elements waste more time to wait for the data from the memory, or partial sum from other PE, their operation must be stalled. This mean that the control flow, Although tasks are allocated to every PE, it is far from fine-grained parallelism. Some of them still need to work in collaboration. there is still room for improvement of the parallelism of each PE.

## Slide 8
Verification &
Analysis (cont.)
Traffic Analysis:
Notes: I also do the traffic analysis, which mainly focus on the usage of each links and the traffic congestion happened in the network. Numbers marked in the graph are the number of how many times the link is used. And by measuring the waiting time at the beginning of each links, we can know the traffic inside the network. And the results indicate that almost no traffic congestion is observed, only under very few situation, packet is stalled at the links between R5 to R7 for at most 2 ns. Although a simple deterministic routing we used, it is totally enough for this design.

## Slide 9
Advance Design
Notes: But there is still much to be improved. One is optimization for sparse input. In Spike neural network, inputs are only spikes, which is either 1 or 0. obviously, for a 0 input, calculation will be wasteful, since the result will always be 0. Therefore, in this design, few additional control logics were implemented to achieve better performance for sparse input. Here the dpkt will counting the sequence of zeros in a row of input feature or filter. These information will be sent to the merge, split and controller. Then during the following operation, data of 0 will not even be read out from the register, and the whole system will just skip these data, to avoid unnecessary calculation.

## Slide 10
Performance
Cumulative time (Sparse) (ns) |  | 
Average time (per step) (ns) |  | 
Average throughput |  | 
Notes: The improvement is significant. Let look at this graph which shows the total time using for 10 timesteps computation. The red and orange line show the cumulative time of normal PE, or say the PE without optimization, Time used for regular and spare input are the same, since whether the input is 0 or not, the PE performs complete operation. And for optimized PE, took less time for regular input, and for sparse input, it is faster. Basically, for a sparse input optimized PE, it only use 2068 nano seconds for finishing 10 timesteps computation. And the average throughput, here in this graph, clearly increasing compares to the normal PE. Basically about 16% improvement can be obtained. And of course, it become not only faster, but also more power efficient.

## Slide 11
Summary &
Outlook
Advantage
Can be Improved
Notes: At last, look back to this project, an asynchronous SNN accelerator is proposed, which could handle a 5 by 5 ……
I did implement the accelerator with torus topology, but unfortunately there isn’t significant improvement under this deign, since the NoC communication of the original topology is already enough . But maybe in the future, when some certain improvement will lead to much heavier data communication, this design will be helpful.
In summary,

## Slide 12
Acknowledgment &
Reference
Reference
Acknowledgment
Notes: I’d like to thank prof ….

## Slide 13
Thank You for Your Listening