## Slide 1: EE552 – Asynchronous VLSI
TA: Matt Conn, (he/him/his), connmatt@usc.edu
March 24th, 2022
Dataflow Options for 3 PEs

## Slide 2: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
Vth = 64*

## Slide 3: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 4: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 0 | 0
0 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 5: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 0
0 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 6: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
0 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 7: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
24 | 0 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 8: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
24 | 52 | 0
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 9: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
24 | 52 | 47
0 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 10: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
24 | 52 | 47
31 | 0 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 11: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Each element of the output is formed with a “matrix-wise” dot product of the kernel, and a same-sized submatrix from the ifmap
Mem | pot | t=1-
62 | 57 | 63
24 | 52 | 47
31 | 30 | 0
These are the membrane potentials from the end of the previous time step – we “resume” by starting each output of this time step at the corresponding value (of course it is 0 everywhere when we “turn on” the machine)
Fixed values for all timesteps
New values at each timestep
T=1

## Slide 12: Recall: kernel strides across ifmap
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Repeating over the entire timestep, and finish by subtracting Vth=64, if necessary, and outputting spikes of 1 or 0
Mem | pot | t=1
62 | 57 | 63
24 | 52 | 47
31 | 30 | 35
Out | Put | t=1
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
T=1

## Slide 13: Recall: kernel strides across ifmap
i | f | m | a | p
0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Repeating over the entire timestep, and finish by subtracting Vth=64, if necessary, and outputting spikes of 1 or 0
Mem | pot | old
62 | 57 | 63
24 | 52 | 47
31 | 30 | 35
Out | Put | t=2
1 | 1 | 1
0 | 1 | 1
0 | 1 | 1
T=2
Mem | pot | t=2-
102 | 107 | 99
63 | 98 | 68
56 | 70 | 76
Mem | pot | +
40 | 50 | 36
39 | 46 | 21
25 | 40 | 41
Mem | pot | t=2
38 | 43 | 35
63 | 34 | 4
56 | 6 | 12
>64? spike &-64

## Slide 14: Option 1: “weight stationary”
Memory Wrapper
Filter weights get loaded from memory only one time
- once in the entire simulation
Input spikes are fetched from memory, shared between PEs, and re-fetched
- multiple times per timestep
Memory
NoC
PE2
PE1
PE3
Adder

## Slide 15: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 16: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 17: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 1
0 | 1 | 1
1 | 0 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 18: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 1
0 | 1 | 1
1 | 0 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 19: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Proposed improvement – grab 2 extra bits, save a trip to memory?
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1

## Slide 20: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 1
0 | 1 | 1
1 | 0 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 21: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 0
1 | 1 | 1
0 | 1 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 22: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10

## Slide 23: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Before next row (of outputs)…

## Slide 24: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 0
1 | 1 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Now: next row (of outputs)…
0 | 0 | 0

## Slide 25: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
1 | 1 | 1
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Final row (of outputs)…
0 | 0 | 0
0 | 1 | 0

## Slide 26: Option 1: “weight stationary”
Memory Wrapper
Memory
NoC
PE2
PE1
PE3
Adder
i | f | m | a | p
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0
ifmap
(x10)
weights/ kernel
(x1)
ke | rn | el
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
14 | 5 | 8
4 | 8 | 7
10 | 9 | 10
Beginning of next timestep…
1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
membrane potentials
(x1)

## Slide 27: Pros/Cons?
Communication with memory:
PE utilization:
Data reuse:

## Slide 28: Other options & larger PE architectures covered further in discussion
row-stationary (Eyeriss)
output-stationary
weight-sharing
ifmap-sharing
Nvidia + Georgia Tech highlight paper
weight reuse
ifmap reuse
data sharing
NoC size + traffic
short, fast packets
long packets
Which of these is the goal?

## Slide 29: Other options & larger PE architectures covered further in discussion
row-stationary (Eyeriss)
output-stationary
weight-sharing
ifmap-sharing
Nvidia + Georgia Tech highlight paper
weight reuse
ifmap reuse
data sharing
NoC size + traffic
short, fast packets
long packets
Which of these is the goal?
Latency, throughput, energy-efficiency, PPA, flexibility/scalability